| TASK: FIRE EXINGTUISHER (USE & INSPECTION) | Overall Task Risk Rating: | C |
| --- | --- | --- |
| Description: | Tucker Hi-Rise utilizes various sized ABC class rated fire extinguishers. These are deployed on all our sites and facilities including our heavy equipment and Foremen vehicles. They are inspected monthly and certified yearly. Their use is for fire mitigation and reduction of fire spread should one occur. |
| Application: | Construction Projects | Industrial (Maintenance Shop, Storage Areas) | Office Areas | Performed By: | Our Organization | Subcontractors |
| Applicable Legislation: | OHSA | Construction Regs. | Industrial Regs. | Designated Substances | Confined Spaces | Asbestos on Constr. |
|  | WHMIS/GHS | Bio and Chem. Agents | Highway Traffic Act | First Aid | Compulsory Trades | Employment Standards |
|  | Other: Building Code, Fire Code Ontario Regulation 213/91. Construction Projects Section 52-58 – Fire Safety |
| Approved By: |  | Position: | PRESIDENT | Date: |  |
| Reviewed By |  | Position: | HEALTH AND SAFETY COORDINATOR | Date: |  |

| Job Hazard and Risk Analysis (JHRA) | RISK RATING SYSTEM RISK | A | High likelihood of personal injury or facility, material or equipment damage. |
| --- | --- | --- | --- |
|  |  | B | Moderate likelihood of personal injury or facility, material or equipment damage. |
|  |  | C | Minor likelihood of personal injury or facility, material or equipment damage. |
| TASK HAZARDS | PRE-TASK RISK RATING | TASK CONTROLS | POST TASK RISK RATING |
| Fires | A | A Daily Job Hazard Assessment (JHA), in conjunction with all subcontractors will be completed and reviewed to ensure all workers on site understand the hot work hazards, fire safety and storage locations. Never allow oil or grease to come contact with oxygen, oxygen-acetylene, equipment or hoses. Do not use flammable materials where there is a potential heat source. Use in a well-ventilated area. Welding or cutting must not be done on containers that have held flammable or poisonous substances until they have been thoroughly cleaned and safeguarded. Obey “No Smoking” signs. | C |
| Equipment Failure | B | Damaged fire extinguisher must be noted, tagged as damaged, taken out of use, and reported to the Site Foreman / Maintenance Foreman immediately. All fire extinguisher operators must be competent and hold valid training certifications. Fire extinguisher shall be operated as per the manufacturer’s instructions. | C |
| Lack of Inspection | C | All fire extinguishers shall be inspected monthly. Inspections shall be recorded on tags, attached to the fire extinguisher. Inspections tags shall not be removed, unless they are filled, and a new tag is immediately installed. Damaged fire extinguisher must be noted, tagged as damaged, taken out of use, and reported to the Site Foreman / Maintenance Foreman immediately. | C |
| Lack of Training | C | All fire extinguisher operators must be competent and hold valid training certifications. | C |
| Lack of Planning | C | Equipment must be stored in designated areas, in close proximity to flammable material, in close proximity to hot-work activities. Fire extinguishers must be in said areas, prior to the storage or commencement of activities. | C |
| Lack of Maintenance | C | Fire extinguisher shall be operated and maintained as per the manufacturer’s instructions. | C |

| Personal Protective Equipment (CSA Approved) |
| --- |
| HEAD PROTECTION | FOOT PROTECTION | EYE PROTECTION | SKIN PROTECTION | FALL PROTECTION | RESPIRATORY PROTECTION | HEARING PROTECTION | HIGH-VIS PROTECTION | HAND PROTECTION | FACE PROTECTION | ADDITIONAL PROTECTION LISTED IN CONTROLS |
| ADDITIONAL PPE CONSIDERATIONS Workers on construction projects must wear, at a minimum, CSA high visibility protection, head and foot protection. Ensure workers wear CSA approved eye protection when completing tasks that may cause objects to fly, dislodge or the like including the use of the quick cut saw. All workers using Chemicals must wear the required personal protective equipment set out in its (M)SDS. Eye protection shall also be worn where equipment does not provide appropriate protection to worker's eyes. Seat belts must be worn at all times by equipment operators, when seat belts are provided. Workers must wear appropriate hearing protection, suitable for the sound levels to, when exposed to 85db or more, over an 8-hour period. Hearing protection is also required when exposed to higher decibels over a shorter period of time. Hearing protection must reduce exposure levels below allowable limits. |

SAFE WORK PRACTICES (SWP)

FIRE EXTINGUISHERS P – Pull the pin. A – Aim at the base of the fire. S – Squeeze the handle. S – Sweep from side to side. Fire extinguishers are classified according to their capacity to fight specific kinds of fires. Class A – for fires in ordinary combustible materials such as wood and paper where you need a quenching, cooling effect. Class B – for flammable liquid and gas res such as oil, gasoline, paint, and grease where you need oxygen exclusion or flame interruption. Class C – for fires involving electrical wiring and equipment where you need a non-conductive extinguishing agent. Class D – for fires in combustible metals such as sodium, magnesium, and potassium. Extinguishers have a very short duration of discharge—usually less than 60 seconds. Within that limited duration, you have got to use the extinguisher effectively. All workers who may be required to use any fire extinguishing equipment will be provided adequate awareness on use and application. All fire extinguishers must be inspected monthly. Do not tamper with fire extinguishers, emergency equipment and/or block emergency exits, signs in the workplace or fire routes in the parking areas. All company approved fire extinguishers are of a suitable types and sizes to permit the evacuation of workers during a fire. Every fire extinguisher shall be of a type, of whose contents are discharged under pressure and have an Underwriters’ Laboratories of Canada 4A40BC rating. When conducting open flame operations, ensure that fire extinguishers are readily available within 10 feet. Fire extinguishers must also be available in locations where flammable or combustible materials are stored, handled, or used, on each storey of an enclosed building being constructed or renovated and in shops for at least every 300 square metres (approx. 3,000 square feet) of floor area. Fire extinguishers must be readily accessible, properly maintained, regularly inspected, and promptly refilled immediately after use. Fire extinguishers must be secured to all mobile equipment. Fire extinguishers must be protected from damage and freezing

FLAMMABLE MATERIALS Flammable liquids must be stored in CSA, UL, FM approved containers with flash arresting caps in place. Containers must be grounded and bonded during decanting. All environmental plans will be followed when disposing of left-over flammable material. All containers containing flammable material will be labelled properly according to the WHMIS regulations. Flammable or combustible materials must be stored in their approved locations. Any hand-held device that needs to be refuelled must be carried to the refuelling station. No process that may cause a spark shall be performing within 100’ of the fuel storage area. All refuelling will be performed when the equipment is not running and in an outdoor location. Employee will wear the required personal protective equipment while refuelling a machine. The flammable storage area must be 50’ away from all buildings. Flammable material will be stored in a location that provides secondary containment to ensure that any leaks that occur do not become an environmental issue. A fire extinguisher shall be stored in close proximity to any flammable material storage area.

FLAMMABLE MATERIAL STORAGE All materials are to be stored in an organized manner and in their designated storage area. Store hazardous materials in their appropriate location. Objects or materials, including garbage, are not to be protruding into aisle-ways or into overhead into work areas. Ensure material is not stored in access/egress corridors or areas. Flammable materials and their containers must also be covered with their appropriate screw on caps and stoppers. Flammable materials and their containers must also be stored in a well-ventilated area. No smoking is permitted in close proximity to flammable material storage areas. Flammable materials and their storage cages or racks must be made available in a safe location away from work areas or buildings. Empty flammable materials and their containers will be stored separately from full or partial containers. Only one day's supply or less of gas or other flammable materials is to be stored indoors, at any time. Use/store and transport all gas and flammable materials containers in a secured and upright position.

FIRE PROTECTION When using salamander heaters, ensure that the following conditions are met: Propane cylinders are placed at least 10' away from the salamander heater or other ignition sources and there are no flammable or combustible materials placed in the vicinity of the heater, (e.g., tarps, wood, straw, gasoline containers, etc.). Propane is stored outdoors and only a normal days’ supply of propane is stored indoors. Fire extinguishers are readily accessible in the area. Properly vented (circulate air in units - open window)

TRAINING Every worker who may be required to use re extinguishing equipment shall be trained in its use. Employee Orientations must include a review of these JHAs. Workers exposed to / or required to work with WHMIS controlled products/material, must be trained in WHMIS accordingly. All equipment operators must be competent and hold valid training certifications for specific pieces of equipment where required by applicable legislation.

PERSONAL PROTECTIVE EQUIPMENT USE, INSPECTION AND MAINTENANCE Workers on construction projects must wear, at a minimum CSA or Equivalent high visibility vest, head, and foot protection. All PPE will be visually inspected by the worker as part of the completion of the Daily JHA. All PPE will be inspected on a weekly basis by the Foreman during the completion of the Weekly Workplace Inspection. All damaged, broken or equipment missing components will be removed prior to use and replaced by the by the company. Workers are responsible with replacing their safety foot protection. All workers using Chemicals, must wear the required personal protective equipment set out in its SDS.

INSPECTIONS All fire extinguishers must be inspected monthly. All equipment operators must conduct and record pre-use inspections where required for specific pieces of equipment. Foremen must conduct weekly inspections (at a minimum) of construction project workplaces. Joint Health and Safety Committee must conduct monthly inspections, of workplaces.

Safe Job Procedures (SJP)

PRE-TASK COMMENCEMENT Complete a daily hazard assessment, in conjunction with all subcontractors, and review with all workers. Ensure all workers understand the daily hazard assessment contents and sign off in acknowledgement. Determine what tasks may require the use of a fire extinguisher. Prior to locating a fire extinguisher in a location, for a particular task or fire protection measures, ensure the fire extinguisher is inspected, and therefore in good working condition. Note inspection of the fire extinguisher, on the attached inspection tag. Do not remove the tag unless the tag is filled, and a new tag is to be installed immediately.

DURING & POST TASK If fire is observed, assess the situation to see if it is safe to attempt to extinguish. If the fire cannot be controlled, initiate the evacuation procedure immediately. Locate the fire extinguisher. Remain calm. Hold the fire extinguisher securely, using two hands. Safely proceed to the fire. Be aware of path to fire and of any obstacles that may inhibit progress. Re-assess the fire, if there is a risk of smoke inhalation, or if visibility is poor initiate the evacuation procedure immediately. Extinguish the fire using the P.A.S.S. method: Pull the pin. Aim at the base of the fire. Squeeze the lever slowly. Sweep from side to side. Always keep at least 3 meters back from the fire, and never turn your back to the fire. Always ensure that you have a clear exit path. If the fire cannot be put out in 10 seconds, do not continue to fight – EVACUATE. Assess the scene to ensure that the fire does not reignite. Inform Foreman or management that the extinguisher needs to be replaced immediately. Tag-out extinguisher and place where it will not be confused for a fully charged extinguisher. Ensure all equipment, machinery and/or tools is maintained and stored appropriately. Store all equipment machinery, tools and material in their designated locations. Implement any housekeeping or maintenance on equipment, machinery and/or tools as required.

Related Workplace Standard References

Housekeeping Equipment and Machinery Operation