| TASK: HOUSEKEEPING | Overall Task Risk Rating: | C |
| --- | --- | --- |
| Description: | Tucker HiRise Contracting Limited’s activities that relate to housekeeping, including maintaining appropriate access and egress, storing material and staging areas, slip and trip hazards and general cleanliness. All employees and Subcontractors are tasked with ensuring sites are monitored and housekeeping hazards are mitigated |
| Application: | Construction Projects | Industrial (Maintenance Shop, Storage Areas) | Office Areas | Performed By: | Our Organization | Subcontractors |
| Applicable Legislation: | OHSA | Construction Regs. | Industrial Regs. | Designated Substances | Confined Spaces | Asbestos on Constr. |
|  | WHMIS/GHS | Bio and Chem. Agents | Highway Traffic Act | First Aid | Compulsory Trades | Employment Standards |
|  | Other: Ontario Regulation 213/91. Construction Projects Section 35-37 – Housekeeping |
| Approved By: |  | Position: | PRESIDENT | Date: |  |
| Reviewed By |  | Position: | HEALTH AND SAFETY COORDINATOR | Date: |  |

| Job Hazard and Risk Analysis (JHRA) | RISK RATING SYSTEM RISK | A | High likelihood of personal injury or facility, material, or equipment damage. |
| --- | --- | --- | --- |
|  |  | B | Moderate likelihood of personal injury or facility, material, or equipment damage. |
|  |  | C | Minor likelihood of personal injury or facility, material, or equipment damage. |
| TASK HAZARDS | PRE-TASK RISK RATING | TASK CONTROLS | POST TASK RISK RATING |
| Improper Disposal of Hazardous Materials | B | All hazardous waste materials must be disposed of according to Provincial Regulations. Consult SDS for specific material considerations. Ensure owners provide Designated Substance Surveys / Soils Reports prior to commencing any work onsite. Consult Designated Substance Surveys and relevant Provincial Regulations for appropriate controls. Never pour chemicals down drains, onto the ground or into sewers. Designated materials must be disposed of in their designated disposal containers, and in accordance with legislated regulations | C |
| Procedures not Followed Lack of Awareness, Knowledge Coordination and Communication | C | All employees must receive orientation and training for General House Keeping procedures and practices. Workers must adhere to all requirements of legislated regulations when handling specific designated substances. Workers must wear all PPE defined in Provincial Regulations when handling specific designated substances as well as stated in SDS material. | C |
| Inappropriate Housekeeping, Accumulation of Dust, | C | Vacuum dust as often as required, and if not specified by legislative requirements as often as possible and at least once daily. Do not sweep dust unless a sweeping compound is used. | C |
| Poor Housekeeping and Site Planning | C | Packaging and debris must not be left to accumulate, dangerous hazards underneath such as protruding nails, faulty wiring or damaged flooring may be hidden. Excessive clutter must be removed to prevalent obstructions makes it difficult to use mechanical equipment resulting in people more likely to handle materials manually unnecessary. | C |
| Improper Storage | B | All tools should be placed in their proper storage area at the end of use or at the end of the day. Equipment, machinery, tools, and material must not be left on any working surface, or in access/egress routes. Store and/or stack material in such a manner as to prevent tipping. Tie down material if there is a risk of it moving inadvertently. Materials are not to be left unprotected and every reasonable precaution must be taken to ensure that the public does not have access to site materials. | C |
| Poor Vehicle Housekeeping | C | Trucks and company vehicles should be cleared daily of any garbage so as not to obstruct brakes, accelerator pedals, stick shifts of windows. All materials / tools shall be secured properly. | C |
| Material Exposure to Weather Improper Storage and Hoarding and Barricades | C | Store and/or stack material in such a manner as to prevent tipping. Tie down material if there is a risk of it moving inadvertently. Ensure Material is not stored in access/egress corridors or areas. | C |
| Improper Lifting Lack of Proper Breaks | C | Use proper material handling techniques to ease fatigue and mitigate repetitive motion effects. | C |

| Personal Protective Equipment (CSA Approved) |
| --- |
| HEAD PROTECTION | FOOT PROTECTION | EYE PROTECTION | SKIN PROTECTION | FALL PROTECTION | RESPIRATORY PROTECTION | HEARING PROTECTION | HIGH-VIS PROTECTION | HAND PROTECTION | FACE PROTECTION | ADDITIONAL PROTECTION LISTED IN CONTROLS |
| ADDITIONAL PPE CONSIDERATIONS Workers on construction projects must wear, at a minimum, CSA high visibility protection, head, and foot protection. Ensure workers wear CSA approved eye protection when completing tasks that may cause objects to fly, dislodge or the like including the use of the quick cut saw. All workers using Chemicals must wear the required personal protective equipment set out in its (M)SDS. Eye protection shall also be worn where equipment does not provide appropriate protection to worker's eyes. Seat belts must be always worn by equipment operators when seat belts are provided. Workers must wear appropriate hearing protection, suitable for the sound levels to, when exposed to 85db or more, over an 8-hour period. Hearing protection is also required when exposed to higher decibels over a shorter period. Hearing protection must reduce exposure levels below allowable limits. |

SAFE WORK PRACTICES (SWP)

HOUSEKEEPING PRACTICES All material and debris shall be cleaned or removed as often as required to maintain an organized and safe worksite. All floors, aisles, stairways, exits, and access to emergency equipment are to be always kept clean and free of obstructions. Each employee is responsible for maintaining and cleaning their work area daily (more frequently if necessary). Keep equipment and areas around the equipment clear of scrap waste and organize the work. If debris is still onsite, pile it out of the way of any access or egress area in a manner that is safe. Before handling lumber, remove or bend over nails and chip away concrete. Keep all areas inside the cabs of machinery free of debris and all windows cleaned. Ensure all chemicals are stored correctly and identified. Store materials away from overhead power lines. Ensure all compressed gas cylinders are stored in an upright manner whether empty or full. Dispose of debris and garbage in designated bins and/or locations. All hazardous waste materials must be disposed of according to Provincial Regulations. Consult SDS for specific material considerations. Identify areas that may remain wet and slippery and post appropriate signage. Trucks and company vehicles should be cleared daily of any garbage so as not to obstruct brakes, accelerator pedals, stick shifts of windows. Packaging and debris must not be left to accumulate, dangerous hazards underneath such as protruding nails, faulty wiring or damaged flooring may be hidden. Excessive clutter must be removed to prevalent obstructions makes it difficult to use mechanical equipment resulting in people more likely to handle materials manually unnecessary. Vacuum dust as often as required, and if not specified by legislative requirements as often as possible and at least once daily.

HOUSEKEEPING AVOIDANCES Do not allow rubbish to free fall from any level of a project unless a safe procedure is in place for doing so. Do not throw tools from one level or another. Do not stack materials in an uneven manner that may result in the material shifting or falling. Do not stack or store any materials closer than 1.8 meters from the edge of a trench or roof. Do not sweep dust unless a sweeping compound is used.

Ice, Snow and Mud Areas of access and egress shall be kept clear of snow, ice, or other slippery material. Areas of access and egress shall be treated with sand or similar material when necessary, to ensure a firm footing. Monitor weather conditions and anticipate when snow / ice clearance may be required. (may be necessary for workers to start work earlier to implement procedures). Prioritized areas for clearing of snow and gritting of paths, steps, and slopes (main access routes, paths from car parks to buildings etc. to be dealt with ASAP). Other areas cleared as time permits. Muddy areas must be cleared or made suitable for safe work. Create direct access to the main entrance from the site access point. Regular inspection of all areas and identification of those such as steps, slopes etc. which may not be safe even when cleared. Treat cleared paths with salt and grit if freezing temperatures continue. Ensure all workers are aware of designated paths / access routes and take responsibility for using these. If slopes and steps remain in a dangerous condition, it may be necessary to prevent access to affected area –cones / barrier/ tape etc. An adequate supply of snow and ice clearance materials will be always maintained on site when the risk of slips and trips is medium too high. For the sake of pedestrian safety and mobility, the snow and ice clearance of sidewalks and walkways around and through the site must be carried out as and when required, to reduce the risk of a slip or trip incident to as minimum level as is possible. Major vehicular routes through the site will remain clear of parked vehicles to allow clear access for both site traffic and the emergency services (if required). Provisions will be made for workers to be able to go to a safe dry area to change into dry clothing as required. Tie down material if there is a risk of it moving inadvertently.

TRAINING Employee Orientations must include a review of these JHAs. Workers exposed to or required to work with WHS controlled products/material, must be trained in WHS accordingly.

PERSONAL PROTECTIVE EQUIPMENT USE, INSPECTION AND MAINTENANCE Workers on construction projects must wear, at a minimum CSA or Equivalent high visibility vest, head, and foot protection. All PPE will be visually inspected by the worker as part of the completion of the Daily JHA. All PPE will be inspected on a weekly basis by the Foreman during the completion of the Weekly Workplace Inspection. All damaged, broken or equipment missing components will be removed prior to use and replaced by the by the company. Workers are responsible with replacing their safety foot protection. Workers must adhere to all requirements of legislated regulations when handling specific designated substances. Workers must wear all PPE listed in specific materials SDS.

INSPECTIONS All equipment operators must conduct and record pre-use inspections where required for specific pieces of equipment. The Foreman must conduct weekly inspections (at a minimum) of construction project workplaces. Joint Health and Safety Committee must conduct monthly inspections, of workplaces.

Safe Job Procedures (SJP)

PRE-TASK COMMENCEMENT Complete a daily hazard assessment, in conjunction with all subcontractors, and review with all workers. Ensure all workers understand the daily hazard assessment contents and sign off in acknowledgement. Determine what equipment, machinery, tools and/or material, are required for the completion of the task. Ensure preventative maintenance activities have been completed where required, prior to using equipment, machinery and/or tools. Inspect all] equipment, machinery and/or tools. Also inspect the intended area of use. Complete appropriate inspections. Document inspections on appropriate forms when required. If equipment, machinery and/or tools are observed to be damaged: document deficiencies, tag equipment, and remove from use. Notify Foreman of damage immediately. Do not operate equipment, machinery and/or tools, if the intended area of use, is unsafe. Review and designate approved material storage and disposal locations at the commencement of projects. Organize the work to reduce debris production. Locate garbage receptacles onsite. If using chutes, ensure they installed as per the manufacturer’s instructions. Wear the appropriate PPE for materials being handled during housekeeping activities. Consult MSDS to determine appropriate PPE. Specific consideration should be given to this step when housekeeping activities involve chemicals, dust, and other health related hazards. Eye protection shall be worn where equipment does not provide appropriate protection to worker's eyes. Workers must wear appropriate hearing protection, suitable for the sound levels to, when exposed to 85db or more, over an 8-hour period. Hearing protection is also required when exposed to higher decibels over a shorter period. Hearing protection must reduce exposure levels below allowable limits.

DURING & POST TASK Conduct housekeeping as often as is necessary and at least once daily. This includes: Keeping all access and egress areas free of debris. Keeping equipment and areas around the equipment clear of scrap waste. Securing material against the wind. If debris is still onsite, pile it out of the way of any access or egress area in a manner that is safe. Ensure all chemicals are stored correctly and identified. Storing materials away from overhead power lines. Ensuring all compressed gas cylinders are stored in an upright manner whether empty or full. Use of mechanical devices when handling heavy objects. Operate equipment machinery and/or tools as per manufacturer's instructions. Site equipment machinery and/or tools is to be operated and maintained by qualified and authorized personnel. Implement other JHAs that apply to the specific work being completed, and the specific hazards onsite. When in operation, do not leave equipment, machinery and/or tools or controls unattended. Once equipment, machinery and/or tools is no longer in operation, implement appropriate storage procedures, turn off the equipment, machinery and/or tools and remove any keys or starting devices. Upon completion of housekeeping activities, store housekeeping tools, equipment, and supplies in the appropriate designated location. Implement any housekeeping or maintenance on equipment, machinery and/or tools as required.

Related Workplace Standard References

Manual Material Movement and Storage Excavation and Trenching Flammable Material & Fire Protection Power and Hand Tools