FALL PREVENTION PLAN

All Employees – Typical fall from heights hazards that are encountered by workers in construction include, however are not limited to the following: Elevator shaft openings Stairwell openings Perimeter openings Roof tops Excavation, trench or caisson openings Work off ladders Elevated work platforms Work off scaffolds Work of mast climbers Suspended access platforms Fall from heights can be eliminated through the use of any of the following control strategies alone and/or in combination with others: When possible, implement policies restricting certain types of work that put workers at a risk of falling from heights. Training on Recognition/Evaluation and Control of falls from heights. Installation of guardrail systems or floor coverings. Use of Travel Restraint system. Use of Travel Restrict system. Use of Fall Arrest systems when necessary. Falls from Heights Plan Policies for prevention of falls from heights: All workers must receive ‘Working at Heights’ training, from a Ministry of Labour approved training provider, prior to the commencement of working at heights. Subsequent retraining must be conducted as required, and at least every 3 years. Workers are not allowed to access any unguarded roof areas, unless a roof plan has been implemented and the worker has received training on the plan. Workers must not enter areas where there are no guardrails or floor coverings protecting floor openings and elevator shafts. The installation of guardrails around openings and handrails on stairs will only be completed by trained workers utilizing travel restraint systems when necessary (This must be done under the direction of the Supervisory Team). Excavation or Trench openings that are not sloped in accordance with the legislative requirements and that a worker could fall into more than 2.4 metres (8 ft.) deep shall be protected by an appropriate barrier (Trade Contractors responsibility). This will be monitored by the Project Management Team and workers. Caissons must be adequately guarded by the Trade Contractor. This will be monitored by the Project Management Team and our workers. Work off ladders will be limited. However, should a worker be required to work off a ladder, the following must be remembered: The ladder must be in safe working condition and must be inspected prior to use. The ladder must be secured (top and bottom) (stabilizers can also be used to assist with stabilization). The ladder must be of an appropriate length and design for the work. Extension ladders must extend 900 millimetres (3 feet) above the floor or landing. Set the ladder up in accordance with the manufacturer’s instructions and at a minimum for extension ladders, at a ratio of between 1: 4 (1 foot out for every 4 feet up) and 1:3 (1 foot out for every 3 feet up). Three-point contact must be maintained while on the ladder at all times. Ladders are generally intended for access and egress, therefore work from ladders should only be short in duration. Maintain clean footwear while ascending or descending from a ladder. Never set up ladders near live electrical conductors. Work off Elevated Work Platforms will only be performed by workers trained in the specific Elevated Work Platform application. Fall protection must be used at all times while in powered elevated work platforms. Travel Restraint and Fall Arrest Components All components in each system must be used as per the manufactures instructions and as a minimum, the systems must include the following: Appropriate anchor points for the type of system in use. A user wearing a full body harness equipped with a lanyard (shock absorbing lanyard preferred for most applications – some exceptions do exist). Lifelines designed for the system (when necessary). Rope grab or other movement control device (when necessary). Self-locking connecting devices to connect various components of the systems. Material to protect the lifeline from being cut, chaffed or abraded (when necessary). Other Fall Protection System Requirements Understand how the system can be used safely and do not hesitate to ask for assistance from you Supervisory Team. Only use the system in accordance with the manufactures requirements. Do not expose the equipment to corrosive materials. Do not expose the equipment to sparks or flames. Do not expose the equipment to sharp edges. Inspect the system and all its components prior to each use. Report any defects of the equipment or absence of devices immediately to your Supervisory Team and only proceed if corrective actions have been taken. If any fall protection equipment has been involved in a fall, it must be taken out of service immediately and sent to the manufacturer for inspection. Fall arrest systems must be set up in a manner which will not allow the worker to hit an object or the level below. Only equipment approved by your Supervisory Team may be used in a fall protection system. Good Fall Protection Practices Always be aware of your surroundings. Never rest up against or push on guardrails. Look where you walk and do not step on floor coverings or other objects that may be on the walking surface as those objects may be hiding a floor opening. Do not walk backwards when you are on a work surface that may contain a floor opening (guarded or not). Always report unguarded openings and/or unsafe floor coverings to your Supervisory Team immediately. Take time to review the following fall rescue procedures and make notes to suit them to your Project conditions. Review the fall rescue plan(s) and make note of the equipment required. Other Project Specific Notes POST THIS INFORMATION

FALL ARREST RESCUE PLAN

IF A WORKER IS OBSERVED SUSPENDED IN A FALL ARREST SYSTEM: Assess the situation – ensure your safety at all times (do not attempt a rescue or enter a work area with an unguarded edge without using an appropriate fall protection system). Only workers trained in rescue operations are allowed to perform rescue operations. Obtain assistance – alert your Supervisory Team, the rest of the crew and the Constructor or Owner. Identify the exact location and the nature of the emergency. If the suspended worker is conscious, try to determine the extent of his/her injuries so that the appropriate emergency services personnel can be notified. Call 9-1-1. The Supervisory Team will designate workers to meet emergency services personnel at the entrance to the Project. Note: Time is of the essence, the rescue plan must be initiated immediately to help prevent potential injury to the fallen worker. OTHER WORKERS MUST: Assist as requested by your Supervisory Team or emergency services personnel. Stay clear of activities. If you are not involved directly in the rescue, remain at a safe distance from any unprotected edges and from the rescue area so as not to interfere with the rescue operations. The status of the affected (injured) worker and further direction will be provided as it becomes available POST THIS INFORMATION Option # 1 - Fall Arrest Rescue – USING A Powered Elevating Work Platform (PEWP) Note: Workers will be prevented from exposure to fall hazards when working from the PEWP using a guardrail system and a full body harness with lanyard connected to an appropriate anchor point as defined in the manufacturer’s operating instructions. If two workers are performing work from the PEWP, lower the platform to ground level so that one worker may dismount from the platform. PEWP are not designed for use by more than two workers at a time. Once the PEWP reaches the ground, the worker dismounting from the platform should only disconnect their lanyard from the D-ring on their full body harness. The other end of the lanyard should remain connected to the anchor point in the platform for use by the suspended worker upon rescue. The worker dismounting is responsible to call 9-1-1 (if necessary). Where necessary attach another lanyard to the anchor point in the PEWP (only one worker should be using the PEWP). Raise the platform to a position directly underneath the suspended worker and slowly continue raising the platform until the suspended worker is inside the guardrails of the platform. NOTE: Extra caution should be taken if the suspended worker is unconscious. If it is suspected that the worker has sustained head or spinal injuries do not move the injured worker, wait until medical help arrives. If the fallen worker is conscious and has not sustained any head or spinal injuries, connect the spare lanyard that is already attached to the anchor point on the PEWP to the D-ring on the back of the suspended worker’s full body harness. Disconnect the existing self-retracting lifeline or lanyard. NOTE: The shock-absorbing lanyard or self-retracting lifeline that the suspended worker is connected to should not be removed until after the suspended worker is safely inside the guardrails of the PEWP. Once the original self-retracting lifeline or shock-absorbing lanyard is disconnected, carefully lower the platform to ground level. At ground level, administer First-Aid to the rescued worker, if necessary. Only trained workers are to administer First-Aid and must have the permission of the rescued worker to do so (if the rescued worker is conscious). Secure the incident scene for further investigation. Notify Construction Health and Safety Manager immediately for direction and notification requirements. Pre-Job Review Is the PEWP available? Yes No Is an PEWP operator available? Yes No Is the equipment in Reasonable Proximity? Yes No PEWP Rescue -- Project Specific Notes: POST THIS INFORMATION Option # 2 - Fall Arrest Rescue – Using an Extension Ladder Note: Extension ladders of the correct length must be on site and available to perform this type of Lower level rescue (3 metres or less). This type of rescue will only be performed if a Power Elevated Work Platform is not available. Rescue of a suspended worker using an extension ladder should only be performed if the suspended worker is conscious and has not sustained any injuries that would prevent him/her from ascending or descending a ladder. Position the extension ladder adjacent to the position of the suspended worker with the appropriate ladder set-up. Carefully secure the ladder at the top and bottom (using 1:4 - 1:3 ratio). Instruct the suspended worker to climb onto the ladder. Vertical Lifeline Fall - lifeline extending to the ground: Once three-point contact is established and maintained on the ladder, the suspended worker will: Ascend to location of the rope grab on the vertical lifeline. Slide the rope grab to waist level. Descend 3-4 rungs. Repeat steps b and c until the ground level is reached. Vertical Lifeline Fall – lifeline NOT extending to the ground Once three-point contact is established and maintained on the ladder, the suspended worker will remain on the ladder until emergency services arrive. Pre-Job Review Is the equipment available? Yes No Is an operator available? Yes No Is the equipment in Reasonable Proximity? Yes No Ladder Rescue -- Specific Notes: POST THIS INFORMATION Option # 3 - Fall Arrest Rescue Assistance – Circulation Relief – Using a Zoom Boom Forklift If a Power Elevating Work Platform is not available, the following procedure has been prepared to aid in the prevention of Suspension Trauma to a worker suspended in a harness. This procedure isn’t intended to be used for raising or lowering the worker, rather simply to provide support until Emergency Services arrive. Circulation Relief – Using a Platform: Step 1 Ideally purchase or build a sturdy platform with guardrails and a means of securing the platform to the carriage of the Zoom Boom Forklift ahead of time and leave on site for Emergency Rescue purposes only. If (A) hasn’t been done, attempt to locate a platform/cage that can be used for this support function. Secure the platform/cage to the carriage of the Zoom Boom Forklift. If (A) & (B) aren’t available, build a sturdy/safe makeshift platform (that can be secured in place) using suitable materials that will help provide support for the worker. Step 2 The Zoom Boom Forklift operator must pick up the platform and secure it to the carriage of the Zoom Boom. The Zoom Boom Forklift operator must then drive to the desired location. The operator will place the machine in “park”, apply the hand brake and carefully lift the platform/cage into position below the suspended worker’s feet (angled slightly back towards the carriage – to prevent the secured platform from slipping). The operator will then inch the platform up slowly to allow for the worker to stand on the platform. The suspended worker must remain secured to the fall arrest system at all times. Await the assistance of emergency response personnel and follow their instructions. Pre-Job Review Is the Sturdy Platform available? Yes No Is a Zoom Lift operator available? Yes No Is the equipment in reasonable proximity? Yes No Forklift/Zoom Lift Relief -- Specific Notes: POST THIS INFORMATION