## Slide 1: Cold Weather Training
October 2023

## Slide 2: Overview
Who is carrying cost?
Key Scopes
Earthwork
Footings/slabs
Elevated slabs
Masonry
Interior Finishes
United Rentals

## Slide 3: Who Holds Cost
Owner vs. Brinkmann held
  Communication!!!
Owner – schedule delay or incur cost?
  Weigh the cost versus delay in each scenario
How are you tracking lost days?
How is this carried with subs?

## Slide 4: Allowance Log

## Slide 5: Earthwork & Foundations
Frost in the soil
Remove & replace
Code-L
Additional rock – crane road maintenance

## Slide 6: Winter Concrete
Winter Concrete Services
  Hot Water
  Concrete Additives
    NCA (Non-Chloride Accelerator), Fly Ash, High Ranger Water reducers, etc
Historical Unit Costs
  Hot Water – $6/CYD
  1% NCA - $5/CYD
  2% NCA – $10/CYD

## Slide 7: Slab on Grade
Frost in soil
Remove & replace – same as soil
  Compacted fill
Ground thaw machine
Blankets
  Labor & touches
  Rental vs Purchase?
    ~$0.40/SF/MO – Rental

## Slide 8: Footings & Slab on Grade Blankets

## Slide 9: Elevated Slab
Similar to SOG
  Hot water
  Blankets
Heating under slab

## Slide 10: Elevated Slab Tenting

## Slide 11: Elevated Slab Tenting

## Slide 12: Masonry
Elevator/stair shafts
Grout temperatures
Tenting

## Slide 13: Temp Heating
Permanent systems versus temporary
Beating winter
Retail in multifamily

## Slide 14: Temp Heating – Permanent
Extend your warranty period on HVAC
Additional filter changes
  Buyout – winter or summer
Permanent power
Exterior facade or temp enclosure
  windows

## Slide 15: Temp Heating – Temporary Systems
Power supply
Gas supply
  Permanent meter
Types of heaters
  Building types will determine
Insurance requirements
Ducting heaters
Labor for moving heaters & filling

## Slide 17
Understanding The Fundamental's
Basic Heating Principles

## Slide 18
CFM - Cubic feet per minute
CFH – Cubic feet per hour
BTU (British Thermal Unit)
Infiltration Heat Loss
Air Change Rate
Ventilation Rate
Design Temperature Difference
“U” Value
Glossary of Terms

## Slide 19
Choosing the right heater for the application
Direct Fired Heater
Verses
Indirect Fired Heater

## Slide 20
Must use 100% outside air for combustion air, (never recirculate)
Natural gas or propane gas only
Best heater for heating large spaces
Will provide higher CFM of low R.H. air
Most units can support over 400’ft of fabric duct
10 to 1 fan induction ratio (Centrifugal Blower)
100% Fuel efficiency
180ºF high fire & 100ºF low fire
Direct Fired Heater

## Slide 21
Fuel oil & natural gas or propane fired
The air can be recirculated
Lower CFM better suited to small area’s
Self contained fuel oil units
Towable up to 1 Million Btu’s/hr
Currently limited to 2 million btu’s/hr output
Most are limited to 100’ft of discharge duct
80% Fuel efficiency
Indirect Fired Heater

## Slide 22
Only 92% of natural gas and propane can be converted to energy the remaining 8% become:
Water Vapor
Carbon Dioxide
Carbon Monoxide
Every Million btu’s of fuel burned will produce:
11.7 gallons of water from natural gas
9.7 gallons of water from propane
Byproducts From Combustion

## Slide 23
Air only knows one thing to equalize itself with the ambient air
The hotter the air the faster it rises upward
The warmer the air the more water it can hold
For every action there is a opposite and equal reaction
Recirculation of the inside air increases infiltration of outside air
Understanding How Air Behaves

## Slide 24
Using outside air for combustion air creates positive pressure on the buildings envelope forcing air through the cracked and crevices
We can calculate the air change rate by dividing the building volume by the equipment CFH
Rules of Thumb
1 air change every 2 hours is the minimum
1 air change every hour up to 1.5 air changes is needed on taller structures
Air Change Rate Requirements

## Slide 25
Current List of Makeup Air Heaters